LOCN	LAT:	12o 41' 05.28"S  	  		WELL NAME:	Bilyara 1 & ST1

LONG:  	124o 30' 20.80"E

EASTING:  663522m E	NORTHING: 	8597260m N 	ZONE:

SHOT POINT:  	850	SEISMIC LINE:	VS-25A	STATUS:    	P & A

ELEVN SF: 	 - 88.4m BSL	DATUM RT:	27m ASL	OPERATOR: 	BHP Petroleum

BASIN:		Browse	TOTAL D:  	2836m	PARTNERS:  	Inpex; Conoco

SPUD DATE: 	3/08/1988         	COMPLN DATE: 	8/11/1988	LEASE:    	NT AC/P7

TARGET:           				DRILLER:    	Zapata

DATA SOURCE: 	WCR, logs			RIG:        	Zapata Arctic

FORMATION TOPS:	(P. V. Grech – Wiltshire Geological Services – 1998)

Age	Formation/Unit	Top Depth	Lithology	Interface

Recent to Tertiary		Barracouta		115.4m

Miocene		Oliver		411.0m

Basal Mbr	683.5m

Eocene		Prion		757.5m

Hibernia	Sand Mbr	929.5m

Hibernia		984.0m

Grebe		1086.5m

Basal Mbr	1243.5m

Paleocene		Johnson		 1283.0m

Cretaceous	Maastrichtian to Campanian	Puffin 	Upper SS	1699.5m

Mudstone	1900.0m

Lower SS	1923.5m

Campanian		Wangarlu	Turnstone	1974.0m

Campanian to Santonian		Fenelon	2122.0m

Santonian to Coniacian		Gibson	2308.0m

Coniacian to Cenomanian		Woolaston	2362.0m

Cenomanian to Albian	Jamieson		2419.0m

Jurassic	Tithonian to Callovian	Vulcan	Frigate	2480.5m

Callovian to Oxfordian		Elang	2687.5m

Total Depth	2836.0m

ENGINEERING DATA:	HOLE AND CASING DATA:

Hole 	Hole	Casing	Casing 	Weight	Grade	Joints	Cement	TOC

Size	Depth	Size	Depth	lb/ft

36”	151m	30”	146m	310	X-52	3	900 sx G at SG 1.9

Grouted 250 sx G at SG 1.9

26”	302m	20”	295m	133	X-56	16	750 sx G at SG 1.5

600 sx G at SG 1.9

17 ½”	1293m	13 3/8”	1091m	68	K-55	82	500 sx G at SG 1.5

480 sx G at SG 1.9

12 ¼”	1578m	9 5/8”	1566m	47	N-80	123	325 sx G at SG 1.9

8 ½”	2749m		Stuck pipe, back off at 2717m.  Log, plug back, sidetrack from 1713m

ST	8 ½”	2836m	7”	2832.5m				275 sx G at SG 1.9	TOL 1463.5m

ENGINEERING DATA:	FITs

Casing Size	Depth	TVD SS	Open Hole Size	Depth	TVD SS	EMW (SG)	Comments

9 5/8”	1566m		8 ½”	1581m		1.31	LOT

ENGINEERING DATA:	PLUGGING DATA

A total of 8 remedial plugs, using 5040 sx G at SG of 1.5 to 1.6 were set in the unstable hole below the 13 3/8” casing shoe, before the 12 /14” hole was drilled to 1578, and cased. Final abandonment plugs were:

Plug No.	Interval	Cement

1	2536m – 2690m	184 sx G at SG 1.9	Tagged		Isolate for sidetrack

3	1709m – 1788m	140 sx G at SG 2.0			For sidetrack

ST	Set bridge plug at 2728m in 7” liner

1	2653m – 2728m	43 sx G at SG 1.9	Tagged

2	1418m – 1495m	73 sx G at SG 1.9	Tagged at 1415m	Across liner lap

Cut 9 5/8” casing at 269m and recovered.

3	230m – 310m	143 sx G at SG 1.9	Tag failed

Set EZSV at 268m in 13 3/8” casing

4	230m – 268m	96 sx G at SG 1.9

Cut 13 3/8” casing at 200m and recovered

Set AGE packer at 200m in 20” casing

4	140m – 199m	328 sx G at SG 1.9	Tagged at 147m

Mechanical cut 20” x 30” casings at 122m	Cut failed

Explosive cut 114m, recovered wellhead, guidebases.

ENGINEERING DATA:	DRILL STEM TESTS:

No	Depth Interval	IFT	ISIT	FFT	FSIT	IFP	ISIP	FFP	FSIP	Recovery

1	2730m - 2738m	misrun

1A	2730m - 2738m	7	72	36	160	3816	3792	3821	3816	FW

2	2715m - 2720m	misrun

2A	2715m - 2720m	8	61	102	47	-	-	-	-	49 bbl fluid - no hydrocarbs.

ENGINEERING DATA:	REPEAT FORMATION TESTS	Valid points only – both hole courses

Depth RDF	Depth TVD	Pressure	Permeability	Temp	Comments

m	m SS	psig	mD	degC

1805.0m	1777.9m	2638.7	483

1850.0m	1812.1m	2705.5	601

1895.0m	1867.6m	2771.9	613

ST	2409.5m	2346.9m	1625.7	8

2600.0m	2572.5m	3765.6	5459

2600.0m	2572.5m	3765.2	4202

2602.0m	2574.5m	3765.4	587			Sampled	Filtrate, trace oil

2612.0m	2584.5m	3768.0	832

2625.0m	2597.5m	3771.6	850

2625.0m	2597.5m	3771.6	498

2636.0m	2608.5m	3774.6	504

2639.0m	2611.5m	3773.6	462

2639.0m	2611.5m	3775.0	1297

2639.0m	2611.5m	3775.8	2415

2640.0m	2612.5m	3776.1	84

2640.3m	2613.3m	3774.4	73

2640.8m	2613.3m	3776.2	16			Sampled	Filtrate, trace oil

2641.0m	2614.1m	3778.8	16			Sampled	Filtrate, trace oil

2683.0m	2655.5m	3836.6	1153

2687.0m	2659.5m	3842.2	711

ST	2690.0m	2597.3m	3771.3	5325

2691.0m	2663.5m	3848.1	1103

2695.0m	2667.5m	3854.1	653

ST	2697.0m	2603.4m	3772.6	2901

ST	2704.0m	2609.5m	3774.3	4543

ST	2707.0m	2612.1m	3775.2	1126

ST	2708.0m	2613.0m	3777.3	1126			Sampled	Oil

ST	2709.0m	2613.9m	3777.0	3088

ST	2711.0m	2615.6m	3778.3	206

ST	2711.0m	2615.6m	3779.3	147

ST	2715.0m	2619.2m	3784.3	368

ST	2718.0m	2621.8m	3785.6	733			Sampled	Filtrate, some oil

ST	2718.0m	2621.8m	3788.4	733

ST	2722.0m	2625.3m	3794.3	320

ST	2725.0m	2628.0m	3796.7	1372

ST	2725.0m	2628.0m	3797.7	371

ST	2727.0m	2629.7m	3799.2	230

ST	2730.8m	2633.0m	3803.5	2208

ST	2731.0m	2633.2m	3804.7	2086

ST	2735.0m	2636.7m	3811.0	7

ST	2737.0m	2638.4m	3812.7	44

ST	2737.0m	2638.4m	3812.9	149

STT	2737.0m	2638.4m	3812.4	14

ST	2742.5m	2643.2m	3843.3	7

ST	2745.5m	2645.8m	3856.3	2

ST	2770.0m	2666.9m	3854.7	210

ST	2775.0m	2671.2m	3861.0	180

ST	2775.0m	2671.2m	3860.7	139

ST	2785.0m	2679.8m	3874.6	365

ST	2785.0m	2679.8m	3873.5	753

ST	2800.0m	2692.5m	3891.8	355

ST	2820.0m	2709.4m	3916.0	71

WIRELINE LOG DATA: 	(Schlumberger - 1988)

1	DLL-SDT-MSFL-GR-SP-AMS		Tool problem – run aborted	Suite 1	Run 1

DLL-SDT-MSFL-GR-SP-AMS		1565.5m -	2705.0m		Run 2

LDL-CNL-ML-NGS-AMS		1565.5m - 	2705.0m		Run 3

Wiper trip

VSP	S	ignal problem – part run only		Run 4

SHDT-GR-AMS		Tool problem – run aborted		Run 5

SHDT-GR-AMS		1565.5m - 	2705.0m		Run 6

VSP					Run 7

Wiper trip

RFT					Run 8

RFT					Run 9

RFT		Tool stuck			Run 10

Fish for RFT tool

Cleanout trip

RFT					Run 11

CST					Run 12

1 ST	DLL-MSFL-SDT-SP-GR-AMS		1710.0m - 	2830.5m	Suite 2	Run 1

LDL-CNL-NGS-ML-AMS		1565.5m -	 2834.0m		Run 2

Wiper trip

RFT					Run 3

Wiper trip

RFT					Run 4

SHDT-GR-AMS		1710.0m - 	2825.0m		Run 5

CST					Run 6

CST					Run 7

7” casing job

CBL-VDL-GR-CCL				Suite 3	Run 1

DIGITAL LOG DATA:	(tape data - Schlumberger, verified & edited by Wiltshire Geological Services 1991)

TEMP 	1711.3m -	2835.9m	DT / DTL	1565.1m -	2814.8m

GR 	    80.2m -	 2811.8m	MRES / MTEM	1653.8m -	 2834.6m

CALS 	1560.1m -	 2824.0m 	MSFL / MSFC 	1565.9m -	 2827.9m

LLD / LLS	1566.0m -	 2831.6m 	SP 	1564.2m -	 2805.1m

CALI 	1560.1m -	 2831.6m 	RHOB / DRHO /PEF 	1566.0m -	 2834.6m

NPHI 	1566.0m -	 2831.6m 	NGS 	1561.2m -	 2838.6m

MRE2 / MTE2 	1561.2m -	 2838.6m

LWD GR 	1715.6m -	 2821.8m 	SN / SNC 	1715.2m -	 2821.5m

ROP / WOB	1711.8m -	 2836.3m	RPM 	1711.8m - 	2836.3m

ROP	326.4m - 	2748.8m	TGAS / CHROMATO	1952.1m - 	3747.6m

ST	ROP	1713.9m - 	2835.7m	TGAS / CHROMATO	1713.3m - 	2835.2m

DEVIATION SURVEY:

Depth	Devn (deg)	Azimuth 	Depth	Devn (deg)	Azimuth

1574m	  0.75	-	1608m	  0.5	342.0

1640m	  0.6	340.0	1673m	  0.5	327.0

1690m	  1.0	-	1692m	  0.6	341.0

1766m	  1.5	  15.0	1793m	  1.7	019.0

1823m	  1.9	  26.0	1850m	  1.7	028.0

1890m	  1.3	  24.0	1983m	  2.8	  30.0

1973m	  3.1	  38.0	2028m	  3.0	  46.0

2072m	  3.1	  49.0	2110m	  2.9	  53.0

2123m	  3.0	-	2109m	  2.9	  53.0

2149m	  3.0	  55.0	2183m	  2.3	  50.0

2222m	  1.4	  47.0	2260m	  1.5	  56.0

2288m	  1.6	  47.0	2315m	  1.4	  41.0

2343m	  1.6	  24.0	2370m	  1.5	  23.0

2398m	  0.9	    1.0	2434m	  0.8	334.0

2462m	  0.6	113.0	2493m	  0.7	313.0

2547m	  0.6	280.0	2574m	  1.0	265.0

2574m	  1.0	266.0	2591m	  1.1	254.0

2630m	  1.0	269.0	2670m	  1.1	271.0

2710m	  0.9	296.0	2732m	  1.1	303.0

ST	1729m	  0.8	  27.0	1739m	  0.8	  52.0

1746m	  0.9	  82.0	1754m	  1.5	132.0

1764m	  2.5	129.0	1775m	  3.1	128.0

1786m	  3.4	122.0	1793m	  3.6	117.0

1803m	  4.0	115.0	1813m	  4.3	115.0

1823m	  4.3	114.0	1833m	  4.4	114.0

1842m	  4.4	114.0	1851m	  4.4	116.0

1859m	  4.5	117.0	1867m	  4.6	117.0

1878m	  5.1	118.0	1881m	  5.2	120.0

1886m	  5.7	119.0	1897m	  5.9	122.0

1907m	  6.2	122.0	1916m	  6.7	120.0

1923m	  7.0	119.0	1934m	  7.6	118.0

1944m	  7.9	119.0	1955m	  8.2	119.0

1963m	  8.3	119.0	1972m	  8.8	118.0

1980m	  9.0	118.0	1989m	  9.2	119.0

1998m	  9.6	119.0	2011m	10.6	121.0

2018m	11.3	123.0	2027m	12.0	124.0

2035m	12.6	125.0	2045m	13.8	126.0

2055m	15.3	128.0	2066m	17.1	129.0

2076m	18.8	129.0	2084m	19.3	129.0

2093m	19.7	130.0	2102m	20.1	130.0

2111m	20.8	129.0	2120m	22.3	130.0

2133m	24.7	130.0	2143m	25.9	131.0

2151m	26.6	131.0	2159m	27.0	130.0

2165m	27.2	129.0	2178m	27.3	129.0

2226m	26.0	127.0	2266m	26.5	126.0

2311m	25.8	121.0	2322m	25.8	121.0

2333m	25.6	122.0	2341m	25.5	122.0

2350m	25.8	121.0	2360m	25.8	121.0

2369m	25.4	121.0	2379m	25.3	121.0

2389m	25.7	121.0	2400m	25.9	120.0

2409m	26.3	121.0	2418m	26.6	121.0

2427m	26.9	122.0	2437m	27.1	122.0

2447m	27.1	122.0	2457m	27.0	123.0

2467m	27.2	125.0	2476m	27.5	127.0

2486m	27.4	128.0	2493m	27.2	129.0

2503m	26.8	130.0	2514m	26.5	130.0

2521m	26.5	129.0	2532m	26.5	129.0

2542m	26.5	129.0	2551m	26.5	130.0

2561m	26.6	130.0	2570m	26.9	129.0

2579m	26.8	129.0	2588m	26.6	129.0

2597m	26.6	129.0	2607m	26.5	130.0

2616m	26.5	131.0	2634m	26.6	131.0

2663m	27.2	132.0	2676m	27.4	132.0

2699m	27.9	131.0	2728m	29.2	129.0

2756m	30.4	129.0	2784m	31.5	128.0

2816m	32.0	126.0	2836m	32.5	126.0

MUD PROPERTIES:

Depth (L)	Fluid Type	SG	Vis.	pH	Fl cc	Rm	Rmf	Rmc

2713m	KCL-Polymer	1.17	52	8.5	6.4	0.091 at 29 deg C	0.073 at 28 deg C	0.125 at 27 deg C

KCL		6%

2830m	KCL-Polymer	1.17	43	10	6.7	0.089 at 27 deg C	0.075 at 25 deg c	0.141 at 24 deg C

KCL		6%

CONVENTIONAL CORE DATA:	All cores in original hole

Core No.	Interval (Driller)	Interval (Log)	Recovery

1	2606.0m – 2624.0m	2610.0m – 2626.3m	16.3m

2	2624.0m – 2642.8m	2628.0m – 2646.8m		18.8m

3	2642.8m – 2660.8m	2646.8m – 2664.5m		17.7m

4	2660.8m – 2678.4m	2664.8m – 2682.3m		17.5m

SIDEWALL CORE POINTS:	(69 shot, 45 recovered in Bilyara 1)

1693.0m	1697.0m	1702.0m	1728.0m	1733.0m	1883.0m	1885.0m	1912.0m	1918.0m	1924.0m	1982.0m	2008.0m	2056.0m	2097.0m	2140.0m	2147.0m	2156.0m	2180.0m	2230.0m	2257.0m	2265.0m	2294.0m	2316.0m	2325.0m	2345.0m	2353.0m	2358.0m	2365.0m	2372.0m	2381.0m	2383.0m	2386.0m	2390.0m	2403.0m	2417.0m	2431.0m	2434.0m	2442.0m	2448.0m	2484.0m	2528.0m	2596.0m	2597.0m	2611.0m	2630.0m

(59 shot, 30 recovered in Bilyara 1 ST1)

2410.0m	2411.0m	2418.2m	2694.5m	2705.0m	2707.0m	2709.0m	2710.0m	2711.0m	2713.0m	2718.0m	2722.0m	2724.0m	2725.0m	2726.0m	2727.0m	2730.0m	2732.0m	2733.0m	2734.0m	2735.5m	2737.0m	2738.5m	2739.5m	2740.8m	2745.0m	2746.4m	2748.0m	2758.0m	2790.0m	2794.5m

PALYNOLOGY:		(Rob Helby)

Depth Range	Zone	Subzone	Age

2353m	C. striatoconus or younger		Coniacian

2381m	P. infusoroides		Turonian

2383m – 2386m	D. multipsinum	1aii	Cenomanian

2390m – 2403m	X. asperatus	1aiii	Vraconian

2417m – 2434m	X. asperatus to P. ludbrookiae 	1aiii / b	Late Albian

2442m – 2661.6m	W. spectabilis		Oxfordian

MICROPALAEONTOLOGY:	(Marj Apthorpe)

Depth Range	Zone	Subzone	Age

1693m			Palaeocene

1728m - 1733m		C13	Late Maestrichtian

1912m - 1918m (?1924m)	C12	Middle Maestrichtian

1982m - 2030m			Maestrichtian undifferentiated	-

2056m - 2140m		? C11	probably Early Maestrichtian

2147m - 2257m		C10 	Late Campanian

2265m		C10/C9 boundary	"mid' Campanian

2297m - 2325m		C7 	Santonian

2345m - 2365m		C6	basal Santonian and Coniacian

just below 2365m - 2372m	upper C5 	Late Turonian

2381m		C3b 	Late Cenomanian

2383m		C3a 	Middle - Early Cenomanian

TEMPERATURES:

Depth Driller	Logger	Temp	Log Type	Time since circ	Circ Time

2745m	2713m	  98.4 deg C	DLL	11.25 hrs	Complex

100.0 deg C	FMS	13.25 hrs

100.0 deg C	LDL	22.25 hrs

101.3 deg C	RFT	  10.5 hrs

ST	2836m	2752m	  95.5 deg C	DLL 	  9.75 hrs	nr

2707m	  98.9 deg C	RFT	      6  hrs

2752m	  99.3 deg C	LDL 	16.75 hrs

2752m	100.2 deg C	FMS 	     13 hrs

The WCR claims an extrapolated BHT of 106 deg C at 2717m

CORE ANALYSIS:	(Core Services Australia)	Analyses at ambient conditions

Depth	Porosity	Permeability	Density		Summation of Fluids

%	mD	Bulk	Grain	Por %	SO	SW

2606.1m	22.4	1213	2.10	2.67	21.5	1.0	35.0

2606.3m	22.1	706	2.14	2.67	21.8	1.0	39.3

2606.6m	21.5	722	2.14	2.67	19.2	0.0	32.3

2606.9m	22.9	1711	2.10	2.67	19.4	0.0	26.0

2607.2m	22.1	1698	2.13	2.67	18.2	0.0	25.8

2607.5m	21.9	1170	2.13	2.67	16.9	0.6	23.9

2607.8m	21.7	620	2.12	2.67	21.5	0.5	38.3

2608.1m	22.1	1081	2.11	2.67	22.5	1.4	38.3

2608.4m	22.2	1335	2.12	2.67	21.5	0.5	36.5

2608.7m	20.8	531	2.13	2.67	20.8	0.0	32.7

2609.0m	21.5	698	2.17	2.67	20.2	0.5	35.3

2609.3m	21.6	1444	2.15	2.66	20.2	0.1	36.1

2609.6m	21.5	1025	2.15	2.66	13.6	0.0	12.6

2609.9m	21.2	1254	2.17	2.66	18.8	0.0	38.0

2610.2m	21.1	1011	2.14	2.67	16.7	0.0	20.5

2610.5m	21.2	775	2.13	2.67	14.9	0.0	15.7

2610.8m	22.1	1549	2.14	2.67	21.2	0.5	37.3

2611.1m	21.5	1363	2.14	2.67	20.5	1.0	38.5

2611.4m	20.7	571	2.14	2.67	20.7	0.0	36.1

2611.7m	21.2	1164	2.14	2.67	19.6	0.0	30.5

2612.0m	21.7	1177	2.12	2.67	21.9	0.0	37.7

2612.3m	22.1	2095	2.17	2.67	19.3	0.0	42.7

2612.6m	21.7	1304	2.13	2.67	19.6	0.0	35.7

2612.9m	22.2	1410	2.12	2.66	21.7	0.0	43.1

2613.2m	19.9	1278	2.12	2.61	20.0	0.0	31.6

2613.5m	19.8	646	2.10	2.67	20.9	0.0	32.0

2613.8m	20.8	791	2.15	2.66	20.6	0.0	36.4

2614.1m	21.6	1492	2.15	2.66	20.8	0.0	41.4

2614.4m	21.2	1334	2.10	2.66	17.5	0.0	38.5

2614.7m	22.1	1633	2.17	2.66	19.8	0.0	37.1

2615.0m	21.2	962	2.14	2.66	20.5	0.0	40.6

2615.3m	22.0	1763	2.11	2.66	21.9	0.0	33.7

2615.6m	21.6	1392	2.10	2.66	17.0	0.0	22.1

2615.9m	21.6	1605	2.12	2.66	21.1	0.0	41.1

2616.2m	22.1	1467	2.11	2.66	18.5	0.0	29.6

2616.5m	22.4	2394	2.20	2.66	14.1	0.0	28.1

2616.8m	22.1	2732	2.07	2.66	22.2	0.0	33.6

2617.1m	22.3	2316	2.10	2.66	21.7	0.0	38.6

2617.4m	21.7	1510	2.13	2.66	21.8	0.0	38.0

2617.7m	22.6	2056	2.12	2.66	16.3	0.0	23.3

2618.0m	23.2	3508	2.15	2.66	22.7	0.0	48.3

2618.3m	23.1	2532	2.09	2.66	22.9	0.0	40.0

2618.6m	22.1	1842	2.14	2.66	17.8	0.0	35.9

2618.9m	22.5	2726	2.14	2.66	20.5	0.0	40.7

2619.2m	23.1	2259	2.13	2.66	15.8	0.0	18.8

2619.5m	21.6	1976	2.12	2.66	20.3	0.0	33.3

2619.8m	20.2	1104	2.14	2.66	19.9	0.0	46.0

2620.1m	22.3	2835	2.10	2.66	21.5	0.0	33.1

2620.4m	22.1	2143	2.11	2.66	25.8	0.0	28.6

2620.7m	22.3	1891	2.14	2.66	20.0	0.0	37.3

2621.0m	22.7	2025	2.13	2.66	22.0	0.0	38.6

2621.3m	21.7	2139	2.10	2.66	22.2	0.0	35.8

2621.6m	25.2	4425	2.07	2.66	19.4	0.0	28.7

2621.9m	22.5	2477	2.12	2.66	19.9	0.0	36.2

2622.2m	20.0	1372	2.11	2.66	19.1	0.0	23.1

2624.1m	22.7	3574	2.06	2.66	20.1	0.0	22.5

2624.4m	23.2	2761	2.09	2.66	21.8	0.0	33.5

2624.7m	23.1	3345	2.07	2.66	23.2	0.0	34.7

2625.0m	20.6	1387	2.12	2.66	21.0	0.0	37.4

2625.3m	19.0	781	2.18	2.66	15.9	0.0	35.5

2625.6m	22.4	2699	2.09	2.66	20.9	0.0	31.0

2625.9m	19.3	786	2.08	2.66	22.2	0.0	35.5

2626.2m	22.4	2021	2.10	2.66	17.3	0.0	20.5

2626.5m	23.2	2212	2.08	2.65	22.8	0.0	25.5

2626.8m	23.0	2625	2.18	2.66	16.6	0.0	34.1

2627.1m	21.7	1484	2.09	2.66	15.7	0.0	17.3

2627.4m	22.2	1654	2.14	2.66	19.5	0.0	40.5

2627.7m	20.6	794	2.07	2.66	22.1	0.0	33.7

2628.0m	22.9	2300	2.11	2.66	21.6	0.0	42.9

2628.3m	23.0	2449	2.18	2.66	14.9	1.5	30.7

2628.6m	22.2	1777	2.13	2.66	22.1	0.0	39.3

2628.9m	23.3	2919	2.08	2.66	16.8	0.0	16.0

2629.2m	22.6	1861	2.08	2.66	16.7	0.0	8.7

2629.5m	23.7	2898	2.10	2.66	19.5	0.0	34.4

2629.8m	24.0	2923	2.14	2.66	19.0	0.0	40.3

2630.1m	24.0	2662	2.08	2.66	23.2	0.0	37.6

2630.4m	21.8	1511	2.15	2.66	20.9	0.0	43.1

2630.7m	23.1	1763	2.10	2.66	22.6	0.0	39.8

2631.0m	19.6	885	2.09	2.67	23.5	0.4	52.2

2631.3m	22.9	1874	2.07	2.66	22.9	0.0	38.8

2631.6m	21.2	1518	2.09	2.66	21.6	0.0	37.6

2631.9m	19.0	278	2.15	2.66	19.8	0.0	38.9

2632.2m	24.0	2613	2.11	2.67	14.9	0.0	35.3

2632.5m	22.6	1321	2.08	2.67	22.9	0.0	40.8

2632.8m	24.3	2481	2.09	2.68	21.4	0.0	39.0

2633.1m	22.8	1685	2.11	2.66	21.2	0.0	34.7

2633.4m	18.3	198	2.12	2.66	19.7	0.0	41.9

2633.7m	23.8	2746	2.14	2.66	21.2	0.0	49.4

2634.0m	24.1	2231	2.16	2.66	20.5	0.0	50.5

2634.3m	22.9	1326	2.45	2.66	21.1	0.0	37.2

2634.6m	22.9	1520	2.20	2.66	20.8	0.0	42.2

2634.9m	8.3	0.8	2.38	2.66	12.7	0.0	48.6

2635.2m	14.6	21	2.32	2.65	9.5	0.0	24.4

2635.5m	19.1	62	2.30	2.66	12.9	1.8	44.5

2635.8m	21.4	204	2.21	2.66	19.3	3.4	37.7

2636.1m	20.3	138	2.19	2.66	20.3	6.5	43.1

2636.4m	21.0	137	2.31	2.66	18.3	8.8	54.0

2636.7m	19.0	147	2.42	2.66	11.3	4.3	62.0

2637.0m	20.4	122	2.22	2.66	19.7	10.1	49.5

2637.3m	16.6	31	2.33	2.66	16.3	5.7	69.7

2637.6m	11.8	3.5	2.35	2.68	15.9	5.2	63.5

2637.9m	16.5	23	2.31	2.65	14.4	5.6	60.7

2638.2m	12.4	1.7	2.34	2.66	5.5	6.3	12.7

2638.5m	17.7	25	2.37	2.65	7.2	0.0	51.9

2638.8m	12.6	0.89	2.44	2.66	4.6	0.0	42.1

2639.1m	19.6	77	2.35	2.65	15.8	3.0	73.9

2639.4m	11.4	0.62	2.43	2.66	13.4	1.8	74.2

2639.7m	14.1	5.9	2.39	2.64	14.4	2.5	76.2

2640.0m	15.3	5.8	2.33	2.65	16.8	1.4	76.3

2640.3m	9.8	0.73	2.40	2.65	10.9	0.0	69.9

2640.6m	14.4	3.1	2.41	2.64	12.3	2.0	74.2

2640.9m	8.6	0.49	2.38	2.64	10.5	4.5	65.5

2641.2m	13.9	2.2	2.45	2.65	12.2	4.0	75.7

2641.5m	17.9	16	2.40	2.64	14.1	3.4	73.1

2641.8m	15.1	5.7	2.38	2.66	13.4	3.5	58.4

2642.1m	15.9	6.9	2.40	2.66	13.4	1.8	71.6

2642.4m	17.3	8.9	2.35	2.65	13.0	3.6	66.9

2642.7m	18.4	12	2.29	2.65	10.8	4.2	60.8

2643.0m	14.0	2.4	2.35	2.64	17.2	4.8	72.1

2643.3m	14.0	3.6	2.02	2.65	13.3	6.1	69.8

2643.6m	17.6	16	2.31	2.65	15.5	7.4	65.2

2643.9m	15.7	3	2.46	2.65	15.8	4.7	79.1

2644.2m	15.9	5.5	2.39	2.65	5.9	0.0	48.5

2644.5m	18.9	23	2.33	2.65	15.5	3.7	70.3

2644.8m	18.1	9	2.27	2.64	17.3	2.6	62.7

2645.1m	13.3	0.87	2.43	2.66	15.1	3.2	81.7

2645.4m	16.1	2.7	2.35	2.65	15.5	0.8	75.6

2645.7m	15.9	2.9	2.42	2.65	13.5	0.0	82.1

2646.0m	14.5	2.1	2.46	2.65	9.3	5.3	71.4

2646.3m	10.2	0.99	2.58	2.70	3.5	7.3	72.8

2646.6m	9.8	0.18	2.36	2.66	15.8	3.0	78.6

2646.9m	17.8	4.4	2.42	2.65	14.8	4.9	71.9

2647.2m	5.9	0.03	2.56	2.68	3.5	7.3	65.9

2647.5m	12.9	0.73	2.89	2.88	6.6	4.3	78.2

2647.8m	15.5	0.77	2.33	2.66	16.0	1.5	79.9

2648.1m	11.1	0.2	2.45	2.66	10.6	4.6	78.2

2648.4m	13.7	0.83	2.52	2.66	7.7	9.8	78.3

2648.7m	17.4	3.1	2.39	2.75	13.4	1.8	78.3

2649.0m	17.7	4.9	2.40	2.68	14.4	1.7	77.9

2649.3m	10.3	0.19	2.53	2.67	7.3	0.0	86.5

2649.6m	14.9	2.1	2.36	2.66	16.2	0.0	79.7

2649.9m	16.8	11	2.38	2.66	15.4	1.5	80.2

2650.2m	12.1	0.28	2.42	2.89	10.8	0.0	62.5

2650.5m	13.5	2.1	2.45	2.65	14.2	1.7	80.6

2650.8m	15.5	1.2	2.38	2.65	15.1	1.6	70.7

2651.1m	7.3	0.17	2.34	2.68	16.2	1.4	73.4

2651.4m	16.0	1.8	2.48	2.66	9.0	2.8	80.1

2651.7m	14.7	1.6	2.44	2.65	11.0	2.2	77.1

2652.0m	16.9	7.7	2.41	2.65	12.3	2.0	72.2

2652.3m	15.8	1.1	2.34	2.68	14.5	1.6	72.3

2652.6m	7.4	0.11	2.56	2.67	6.6	11.5	80.5

2652.9m	6.8	0.06	2.60	3.08	12.1	2.1	72.5

2653.2m	6.2	0.12	2.58	2.64	2.4	21.4	53.5

2653.5m	12.4	0.48	2.70	2.66	7.4	3.6	86.6

2653.8m	15.3	1.6	2.35	2.65	16.1	1.5	74.0

2654.1m	7.3	0.12	2.54	2.68	6.7	7.5	86.0

2654.4m	11.4	0.15	2.69	2.67	9.6	8.3	80.7

2654.7m	8.1	0.06	2.56	2.68	7.4	6.9	86.2

2655.0m	17.1	2.5	2.35	2.66	14.7	1.6	70.4

2655.3m	9.9	0.07	2.46	2.70	8.6	2.8	76.5

2655.6m	10.1	0.13	2.57	2.67	6.9	9.3	85.7

2655.9m	9.8	0.14	2.50	2.74	8.9	5.6	84.3

2656.2m	8.9	0.12	2.50	2.68	9.0	6.9	82.8

2656.5m	6.7	0.06	2.54	2.67	5.2	9.7	77.7

2656.8m	12.9	0.43	2.38	2.66	15.6	1.5	83.9

2657.1m	14.1	0.89	2.37	2.83	15.4	0.0	81.2

2657.4m	9.4	0.08	2.53	2.67	7.9	4.8	86.4

2657.7m	8.2	0.08	2.51	2.70	8.3	4.5	84.3

2658.0m	11.8	0.13	2.49	2.66	7.9	1.6	88.1

2658.3m	12.9	0.29	2.43	2.67	8.4	2.9	74.5

2658.6m	14.0	0.41	2.50	2.66	10.3	2.4	87.3

2658.9m	14.6	0.55	2.43	2.66	12.3	2.0	79.1

2659.2m	7.6	0.06	2.53	2.68	3.1	0.0	80.8

2659.5m	9.0	0.06	2.52	2.67	8.3	6.0	84.5

2659.8m	7.7	0.07	2.52	2.66	7.0	7.2	82.8

2660.1m	11.1	0.08	2.47	2.69	11.2	4.4	83.3

2660.4m	8.1	0.09	2.55	2.67	6.8	7.4	85.4

2660.7m	8.9	0.09	2.43	2.67	9.0	4.0	88.6

2661.0m	9.1	0.12	2.46	2.66	8.0	3.0	85.4

2661.3m	9.6	0.1	2.45	2.67	7.7	3.2	85.7

2661.6m	8.3	0.07	2.47	2.69	8.2	6.0	84.1

2661.9m	10.5	0.14	2.34	2.68	8.1	5.7	74.6

2662.2m	9.1	0.09	2.42	2.69	5.7	8.5	80.4

2662.5m	9.4	0.1	2.45	2.68	8.0	4.6	85.4

2662.8m	8.0	0.07	2.49	2.69	7.5	6.6	85.8

2663.1m	8.3	0.08	2.44	2.69	5.7	6.4	80.5

2663.4m	10.4	0.18	2.40	2.73	7.4	6.4	80.4

2663.7m	7.6	0.07	2.48	2.68	9.1	2.7	89.7

2664.0m	10.1	0.21	2.44	2.67	11.5	2.1	91.2

2664.3m	7.3	0.09	2.43	2.69	6.0	8.1	72.5

2664.6m	7.5	0.08	2.51	2.67	7.0	0.0	85.3

2664.9m	12.3	0.33	2.46	2.67	6.7	3.7	84.0

2665.2m	8.4	0.08	2.50	2.69	6.1	4.0	85.0

2665.5m	8.5	0.09	2.39	2.68	12.7	1.9	84.6

2665.8m	12.2	0.34	2.43	2.68	9.6	2.5	82.9

2666.1m	13.0	0.38	2.31	2.67	15.1	0.8	79.7

2666.4m	15.1	0.96	2.39	2.67	11.5	2.1	85.1

2666.7m	12.4	0.49	2.34	2.68	12.9	1.8	79.8

2667.0m	14.5	1.4	2.29	2.67	15.9	1.4	81.8

2667.3m	11.6	0.32	2.46	2.67	9.0	2.7	84.7

2667.6m	12.3	0.29	2.40	2.67	11.3	2.1	84.8

2667.9m	15.9	1.5	2.33	2.66	13.8	1.7	84.0

2668.2m	12.5	0.19	2.31	2.66	6.4	3.6	50.0

2668.5m	12.2	0.19	2.48	2.66	11.6	4.3	81.1

2668.8m	9.8	0.12	2.55	2.70	6.5	3.9	85.7

2669.1m	8.6	0.07	2.51	2.67	8.6	5.8	81.5

2669.4m	10.3	0.15	2.46	2.67	10.7	4.6	82.7

2669.7m	7.8	0.06	2.52	2.68	8.4	6.0	86.5

2670.0m	5.7	0.08	2.58	2.67	6.5	7.9	87.1

2670.3m	6.1	0.09	2.52	2.65	2.2	0.0	79.6

2670.6m	8.7	0.07	2.54	2.66	4.6	0.0	87.3

2670.9m	4.6	0.59	2.54	2.63	5.3	4.8	90.3

2671.2m	4.8	0.16	2.55	2.62	6.1	8.3	87.6

2671.5m	6.8	0.05	2.54	2.64	7.0	14.3	78.8

2671.8m	6.1	0.05	2.43	2.63	11.0	2.2	81.7

2672.1m	10.8	0.12	2.50	2.65	9.9	5.0	87.8

2672.4m	14.0	0.4	2.41	2.65	13.4	1.8	80.8

2672.7m	11.6	0.12	2.45	2.65	7.0	7.0	77.1

2673.0m	7.0	0.04	2.50	2.66	7.0	7.1	85.3

2673.3m	5.7	0.12	2.57	2.67	7.7	13.3	79.8

2673.6m	5.0	0.28	2.58	2.65	5.2	9.8	83.1

2673.9m	13.1	946	2.30	2.93	20.7	0.0	88.9

2674.2m	23.1	4267	2.27	2.66	16.5	0.0	88.0

2674.5m	22.8	4489	2.24	2.66	21.1	0.0	87.9

2674.8m	23.2	3551	2.24	2.65	21.8	0.0	90.1

2675.1m	23.0	2374	2.25	2.65	24.1	0.0	82.8

2675.4m	22.5	1664	2.26	2.65	21.5	0.0	86.2

2675.7m	21.3	1994	2.30	2.66	22.2	0.0	86.0

2676.0m	15.0	1004	2.36	2.74	14.8	0.0	69.8

2676.3m	20.9	1403	2.28	2.65	18.5	0.0	84.8

2676.6m	15.7	219	2.32	2.66	18.2	0.0	86.2

2676.9m	19.7	1481	2.28	2.67	22.3	0.0	80.6

2677.2m	22.9	3166	2.23	2.66	21.1	0.0	85.5

2677.5m	22.2	2620	2.26	2.66	21.0	0.0	84.7

2677.8m	23.5	3695	2.25	2.67	21.1	0.0	84.8

2678.1m	23.0	3164	2.24	2.66	21.4	0.0	85.5

SOURCE ROCK DATA:	(Analabs)	Pyrolysis data

Depth	TOC	Tmax	S1	S2	S3	PI	PC	HI	OI

2147.0m	0.28

2196.0m	0.37

2257.0m	0.33

2345.0m	0.11

2353.0m	0.11

2365.0m	0.06

2381.0m	0.20

2383.0m	0.13

2386.0m	0.46

2390.0m	0.15

2397.0m	0.38

2410.0m	0.61

2417.0m	0.45

2431.0m	0.46

2434.0m	0.45

2442.0m	1.40	433	0.25	2.74	1.71	0.08	0.25	196	122

2448.0m	1.20	430	0.18	2.05	1.58	0.08	0.19	171	132

2457.0m	0.80	432	0.20	1.08	5.29	0.16	0.11	135	661

2466.0m	1.10	431	0.28	1.81	5.47	0.13	0.17	165	497

2475.0m	0.64

2487.0m	1.30	428	0.57	2.41	5.71	0.19	0.25	185	439

2496.0m	1.60	428	0.66	3.40	7.21	0.16	0.34	213	451

2505.0m	0.97	428	0.37	1.70	4.49	0.18	0.17	175	463

2514.0m	0.85	428	0.30	1.32	6.20	0.19	0.13	155	729

2528.0m	1.95	430	0.36	3.16	0.84	0.10	0.29	162	43

2535.0m	1.05	429	0.30	1.71	5.5	0.15	0.17	163		524

2547.0m	1.10	430	0.41	2.19	4.45	0.16	0.22	199	405

2556.0m	1.05	429	0.37	1.77	4.63	0.17	0.18	169	441

2565.0m	0.81	428	0.22	0.94	6.05	0.19	0.10	116	747

2579.0m	0.62

2586.0m	0.64

2596.0m	1.15	427	0.50	1.70	0.94	0.23	0.18	148	82

2646.3m	1.05	428	0.31	1.56	0.85	0.17	0.16	149	81

2653.2m	0.96	429	0.24	1.52	0.87	0.14	0.15	158	91

2664.6m	1.25	430	0.26	2.33	1.56	0.10	0.21	186	125

2670.0m	1.15	429	0.22	2.40	3.84	0.08	0.22	209	334

HYDROCARBON SHOWS:

Interval	Show

2565m – 2611.5m	Gas in poor reservoirs.

2611.5m – 2614.5m	Oil in poor reservoir

2614.5m – 2629m	Residual oil column

DST performance was poor, but core and RFT data indicate that the reservoir is of good quality.

GAS ANALYSIS:	(Core Labs. International)

Sample Type	RFT

Depth	Top	2602m

Component mol %

CO2		6.42

N2		0.61

C1		78.87

C2		5.26

C3		2.78

iC4		0.67

nC4		1.47

iC5		0.80

nC5		0.76

C6		0.78

C7+		1.58

Gas Gravity (Air = 1)	0.798

WATER ANALYSIS: 	A range of “water” analyses are in the WCR; KCL content indicates all such fluids are effectively 100% mud filtrate

WHOLE OIL ANALYSIS:	Oil was recovered on RFT (at 2708m) but there is no analysis in the WCR.

VITRINITE REFLECTANCE:	(Analabs)

Depth	Av Rv max	Range Riv		Av Ri max	Range Ri

2257.0m	0.50	0.48	-	0.51	1.28	0.72	-	1.60

2386.0m	0.50	0.50	-	0.50	1.24	0.80	-	1. 72

2410.0m	0.54	0.51	-	0.59	1.28	0.72	-	1. 78

2442.0m	0.51	0.44	-	0.62

2496.0m	0.49	0.41	-	0.62

2547.0m	0.51	0.43	-	0.57

2596.0m	0.52	0.46	-	0.65

2664.6m	0.52	0.46	-	0.62

VELOCITY SURVEY:	(SSL)	OWT, vertically corrected, relative to SRD (MSL)  Assumes vertical hole

Depth	TVD SS	OWT(sec)	Depth	TVD SS	OWT(sec)

1400.0m	1373.0m	0.5131	1500.0m	1473.0m	0.5346

1560.0m	1533.0m	0.5476	1580.0m	1553.0m	0.5519

1600.0m	1573.0m	0.5572	1620.0m	1593.0m	0.5612

1640.0m	1613.0m	0.5657	1660.0m	1633.0m	0.5694

1680.0m	1653.0m	0.5746	1700.0m	1673.0m	0.5790

1720.0m	1693.0m	0.5841	1740.0m	1713.0m	0.5898

1760.0m	1733.0m	0.5962	1780.0m	1753.0m	0.6026

1800.0m	1773.0m	0.6087	1820.0m	1793.0m	0.6147

1840.0m	1813.0m	0.6212	1860.0m	1833.0m	0.6274

1880.0m	1853.0m	0.6334	1900.0m	1873.0m	0.6397

1920.0m	1893.0m	0.6444	1940.0m	1913.0m	0.6499

1960.0m	1933.0m	0.6552	1980.0m	1953.0m	0.6615

2000.0m	1973.0m	0.6676	2020.0m	1993.0m	0.6746

2040.0m	2013.0m	0.6809	2060.0m	2033.0m	0.6875

2080.0m	2053.0m	0.6946	2100.0m	2073.0m	0.7021

2120.0m	2093.0m	0.7082	2140.0m	2113.0m	0.7146

2160.0m	2133.0m	0.7225	2180.0m	2153.0m	0.7279

2200.0m	2173.0m	0.7331	2220.0m	2193.0m	0.7386

2240.0m	2213.0m	0.7449	2260.0m	2233.0m	0.7519

2280.0m	2253.0m	0.7586	2300.0m	2273.0m	0.7645

2320.0m	2293.0m	0.7701	2340.0m	2313.0m	0.7760

2360.0m	2333.0m	0.7825	2380.0m	2353.0m	0.7874

2400.0m	2373.0m	0.7950	2420.0m	2393.0m	0.8021

2440.0m	2413.0m	0.8079	2460.0m	2433.0m	0.8135

2480.0m	2453.0m	0.8196	2500.0m	2473.0m	0.8248

2520.0m	2493.0m	0.8300	2540.0m	2513.0m	0.8357

2560.0m	2533.0m	0.8410	2580.0m	2553.0m	0.8464

2600.0m	2573.0m	0.8517	2620.0m	2593.0m	0.8570

2640.0m	2613.0m	0.8617	2660.0m	2633.0m	0.8672

2680.0m	2653.0m	0.8722	2700.0m	2673.0m	0.8770

BIT RECORD:

No	Size	Make	Type	Jets	Out	Made	Hrs	WOB	RPM	PP	Condition

klbs	psi

1	26"	Reed	S3SJ	3x28	151m	39m	7	5	100	-	-

36"	Sec	-	3x14	151m	-	-	-	-	-	-

RR1	26"	Reed	S3SJ	3x28	151m	0m	0	5	100	-	wiper trip

2	17 ½"	Sec	S44G	3x24	302m	215m	17.5	15	100	1550	1-1-I

3	17 ½"	Sec	S44G	3x32	326m	24m	2.5	15	100	1550	1-1-I

4	17 ½"	Sec	S44G	3x32	1016m	690m	55.5	10	100	900	3-4-1/16"

4	17 ½"	Smith	S84	3x20	1293m	277m	24.0	45	100	1700	-

5	17 ½"	Smith	S84	3x32		0m	0	45	100	1700	reamed

6	17 ½"	Smith	S84	3x32		0m	0	45	100	1700	1-2-I

7	8 ½"	?	FVH	3x32		0m	0	0	-	1000	clean out

8	12 ¼"	Sec	M44NG	3x32	1297m	4m	2.5	20	100	2000	3-1-I

8RR1	12 ¼"	Sec	M44NG	3x32		0m	0	20	100	2000	-

8RR2	12 ¼"	Sec	M44NG	3x32		12m	2.5	20	100	2000	-

8RR3	12 ¼"	Sec	M44NG	3x32	1093m	1m	0.5	20	100	2000	-

8	12 ¼"	Smith	SVH	3x32	1093m	2m	0.5	25	110	1100	-

9	12 ¼"	Smith	SVH	3x32	1121m	32m	2.5	25	110	1100	-

9	12 ¼"	Smith	SVH	3x32	1578m	457m	52.5	25	110	1100	5-4-1/8"

10	12 ¼"	Smith	SVH	3x32	1578m	0m	0.0	25	110	1100	5-4-1/8"

11	8 ½"	Sec	M44NG	3x32	1600m	118m	17.5	25	100	595	1-1-1

12	8 ½"	Sec	M44NG	3x32	1692m	92m	18.0	25	110	680	3-3-I

13	8 ½"	Sec	S84F	3x11	2126m	434m	45.0	35	90	1680	1-4-1/8"

13	8 ½"	Longyear	DP13	3x9	2145m	19m	7.0	30	90	-	5% worn

14	8 ½"	Sec	S84F	3x11	2460m	315m	65.5	45	180	1650	3-5-1/16"

14	8 ½"	Sec	S84F	2x10,11	2606m	146m	27	45	180	1200	in hole

15	8 ½"	DB	CT303	- - - 	2624m	18m	3	15	110	88	-

15	8 ½"	DB	CT303	- - -	2642m	18m	2.5	15	110	88	-

15	8 ½"	DB	CT303	- - -	2660m	18m	3	15	110	88	15% worn

15	8 ½"	DB	CT303	- - -	2678m	18m	4	15	110	88	25% worn

16	8 ½"	Sec	S86F	2x10,11	2705m	27m	4.5	0	-	3100	in hole

16	8 ½"	Sec	S86F	2x10,11		44m	9	0	-	3100	in hole

17	8 ½"	Sec	S84F	3x14	2836m	0m	0	45	180	1200	wiper trip

18	8 ½"	Longyear	DP15	3x12	1900m	191m	40	20	160	1500	80% worn

19	8 ½"	Sec	S84F	3x14	2007m	107m	28	35	170	1600	1-4-1/8"

19	8 ½"	Sec	S84F	3x14	2184m	177m	35	35	180	1350	1-4-I

20	8 ½"	Sec	M44NG	3x12	2190m	6m	1.5	30	-	1300	6-1-I

21	8 ½"	Sec	S84F	3x32	2836m	0m	0	45	180	1650	wiper trip

21	8 ½"	Sec	S84F	3x14	2836m	0m	0	45	180	1650	wiper trip

21	8 ½"	Sec	S84F	3x14	2378m	188m	36	25	160	1300	1-7-I

21	8 ½"	Sec	S84F	3x14	2541m	163m	32.5	25	180	1450	1-3-1/16"

21	8 ½"	Smith	F27	3x14	2695m	154m	33	30	180	1600	2-8-1/4"

21	8 ½"	Sec	S84F	3x14	2836m	141m	20.5	20	175	1660	in hole

22	8 ½"	Sec	S84F	3x32	2836m	0m	0	45	180	1650	wiper trip

22	8 ½"	Sec	S84F	3x32	2836m	0m	0	45	180	1200	wiper trip

23	6"	Smith	FDG	3x24	2728m	0m	0	0	-	-	wiper trip

24	6"	Smith	FDG	3x24	2728m	0m	0	0	-	-	-

COMMENTS: 	Located 2.9 km west of Montara 1 and 17.4 km SE of Swift 1, testing a western culmination on the Montara structural complex.  The well encountered a gas and oil column in the Montara Formation reservoir target, but reservoir properties are poor, and the well failed to flow on DST.  Permeabilities indicated from RFT are suspect.

WELL SITE GEOLOGIST(s): 			E. Pattillo, W. Yacopetti, A. Ribeiro

WELL DATA SUMMARY PREPARED BY:	WGS -15 May 1998 	(BC/LR)  Revised 24 May 2016 (MJW)